## Slide 1: Maintenance and use of ctu retrievable packer
By :
Jalal Alali
Summer 2018

## Slide 2: work content
Overview
preparation
Tool maintenance process
End of maintenance

## Slide 3: Overview
Introduction of Thru-Tubing Retrievable Packer
Through the tubing packer, the tubing packer can pass through the tubing with a smaller inner diameter and pump pressure to expand and set up its own rubber, thereby achieving a temporary sealing of the target well and the target horizon. Block the blockage and then pump the liquid through the packer to the bottom of the silo. The packer can be housed inside a conventional tubing and within a larger casing below the tubing, and is typically used in routine workover operations

## Slide 4: preparation
2-1 Required documents
2-1-1 Pre-Work Safety Record Sheet, See QHSE System Document,
2-1-2 Make a Tool Status label

## Slide 5: preparation
2-2 Inspection Tool log sheet
Check the operation log table and run the record table to record the operation of the tool in detail, it can be used as a tool to maintain and solve specific problems, Review tool operation records before maintenance
Note: a) The tool must be maintained after use
b) Always check maintenance records before use

## Slide 6: preparation
2-3 Preparation tool maintenance records
After the maintenance of the tool is completed, it is necessary to record the seals and metal parts for maintenance and replacement so that the user can understand the state of the tool after repair, analyse and judge the tool failure when problems occur, and find a solution to the problem.

## Slide 7: preparation
2-4 prepare the assembly drawing

## Slide 8: preparation
2-5 Required auxiliary equipment and related Hand tools:

## Slide 9: preparation
Retrievable Packer Parts list

## Slide 10: Tool maintenance process
No | Tool Name | Quantity | Note
1 | Vise | 1 | 
2 | 24”Pipe wrenches | 2 | 
3 | Adjustable wrench | 1 | 
4 | Allen wrench | Some | 
5 | Common Hand Tools | some | 
6 | O ring special tools | 1 | 
Thru-Tubing Retrievable Packer Tool maintenance special tools and commonly used hand tools
RTV Packer maintenance hand tool preparation

## Slide 11: Tool maintenance process
2-5 Safety related requirements
2-5-1 the maintenance place is an indoor maintenance place. Try to avoid the maintenance of windy weather.
2-5-2 Safety identification inspections include, but are not limited to: (1) wearing PPE; (2) avoiding mechanical injuries and the like.

## Slide 12: Tool maintenance process
3-1 Removal steps
3-1-1 Disassemble the fishing neck [60] and Equalizing sub [64]
fishing neck (60)
Equalizing sub (64)

## Slide 13: Tool maintenance process
3-1 Removal steps
3-1-2 Remove the Equalizing sub [64] and Equalizing sub connector[65]]
Equalizing sub(64)
Equalizing sub connector (65)

## Slide 14: Tool maintenance process
3-1 Removal steps
3-1-3 Remove the Equalizing sub connector [65] from the upper Mandrel [30]
Equalizing sub connector
upper Mandrel

## Slide 15: Tool maintenance process
3-1 Removal steps
3-1-4 Remove the shear screw (17) on the Equalizing sub[64]
shear screw (17)
Equalizing sub(64)

## Slide 16: Tool maintenance process
3-1 Removal steps
3-1-5 Separation of Equalizing sub [64] Equalizing sleeve[61] by shock
Equalizing sub(64)
Equalizing sleeve(61)

## Slide 17: Tool maintenance process
3-1 Removal steps
3-1-6 Equalizing sub part has been disassembled
Equalizing sub(64)
Equalizing sub connector(65)

## Slide 18: Tool maintenance process
End Cap (19)
Bumper Housing (20)
3-1 Removal steps
3-1-7 Remove the end cap [19] from the Bumper Housing[20]

## Slide 19: Tool maintenance process
3-1 Removal steps
3-1-8 Remove the Bumper Housing [20] from the collet sub [24]
Bumper Housing [20]
collet sub [24]

## Slide 20: Tool maintenance process
3-1 Removal steps
3-1-9 Remove the upper mandrel [30] from the upper mandrel connector [21]
upper mandrel [30]
upper mandrel connector[21]

## Slide 21: Tool maintenance process
3-1 Removal steps
3-1-10 Remove the piston [22] from the upper mandrel connector[21]
piston [22]
upper mandrel connector[21]

## Slide 22: Tool maintenance process
3-1 Removal steps
3-1-11 Remove the upper mandrel connector[21] from the pull release sleeve [23]
upper mandrel connector[21]
pull release sleeve [23]

## Slide 23: Tool maintenance process
3-1 Removal steps
3-1-12 Remove the split ring [28] in the pull release sleeve [23]
Split Ring[28]
Pull release sleeve[23]

## Slide 24: Tool maintenance process
Pull release sleeve[23]
Shear screw [38]
3-1-13 Remove the shear screw [38] on the pull release sleeve [23]
3-1 Removal steps

## Slide 25: Tool maintenance process
3-1 Removal steps
3-1-14 Remove the pull release sleeve
Pull release sleeve[23]

## Slide 26: Tool maintenance process
Shear sub[42]
Mandrel [36]
3-1-15 separate the shear sub [42] from mandrel[36]
3-1 Removal steps

## Slide 27: Tool maintenance process
Shear screw[18]
Seat catcher[44]
3-1-16 remove all of the shear screws[18] on the seat catcher[44]
3-1 Removal steps
Shear sub[42]

## Slide 28: Tool maintenance process
Shear sub[42]
Seat catcher[44]
3-1-17 Separate the shear sub[42] from the seat catcher[44]
3-1 Removal steps

## Slide 29: Tool maintenance process
3-1 Removal steps
3-1-18 remove the shear sub[42]and ball seat [45] from the seat catcher[44]
Shear sub[42]
Seat catcher[44]
Ball seat[45]

## Slide 30: Tool maintenance process
Shear adapter[57]
Bottom sub[33]
Shear screw[56]
3-1 Removal steps
3-1-19 remove the shear screw[56]and drag out shear adapter [57] from the mandrel

## Slide 31: Tool maintenance process
Shear adapter[57]
Shear screw [56]
Shear ring [58]
3-1 Removal steps
3-1-20 separate the shear adapter [57] and shear ring [56]

## Slide 32: Tool maintenance process
Bleeder plug[34]
Bottom sub[33]
3-1 Removal steps
3-1-21 Remove the bleeder plug [34] from bottom sub [33]

## Slide 33: Tool maintenance process
Element[32]
Bottom sub[33]
3-1 Removal steps
3-1-22 separate the element [32] from bottom sub [33]

## Slide 34: Tool maintenance process
Element[29]
Element[32]
3-1 Removal steps
3-1-23 separate the element [32] from mandrel [ ]

## Slide 35: Tool maintenance process
Poppet housing[40]
Spring housing[29]
3-1 Removal steps
3-1-24 separate poppet housing[40]from spring housing[29]

## Slide 36: Tool maintenance process
Delayed inflate ring[37]
Spring housing[29]
Shear screw[16]
3-1 Removal steps
3-1-25 Open shear screw[16] and separate delayed inflate ring [37]from spring housing[29]

## Slide 37: Tool maintenance process
poppet[25]
Poppet spring[31]
Poppet housing[40]
3-1 Removal steps
3-1-26 Remove Poppet Housing[40] from Poppet spring[31]

## Slide 38: Tool maintenance process
Latch sub[27]
Mandrel[36]
3-1 Removal steps
3-1-27 Remove poppet housing[40]from mandrel[36]

## Slide 39: Tool maintenance process
Latch sub[27]
3-1 Removal steps
3-1-28 Remove Latch sub[27] from mandrel[36]

## Slide 40: Tool maintenance process
Poppet housing[40]
Collet sub[24]
3-1-29 Separate the collet sub [24] and the poppet housing [40]
3-1 Removal steps

## Slide 41: Tool maintenance process
Poppet housing[40]
poppet[25]
Poppet spring[31]
3-1-30 Remove the poppet[25] and poppet spring[ from poppet housing[40]
3-1 Removal steps

## Slide 42: Tool maintenance process
3.1 Inspect all O-rings on each component for damage.
3.2 After using diesel oil to remove oil from the components of the tool, clean it with clean water and blow it with compressed air, especially to ensure that the inner wall of the tool barrel is clean.
3.3 Check all parts for damage.
3.4 Replace the damaged part and record the part number of the newly replaced part on the maintenance log sheet.
3.5 Apply a little oil on the surface of each spring and O-ring

## Slide 43: Tool maintenance process
3-2 installation steps
3-2-1 Connect the collet sub [24] to the poppet housing [40]
Collet sub [24]
Poppet housing[40]

## Slide 44: Tool maintenance process
Poppet housing[40]
poppet[25]
3-2 installation steps
3-2-2 Connect the collet sub [24] to the poppet housing [40]

## Slide 45: Tool maintenance process
3-2-3 Connect Latch sub[27] to Mandrel[36]
3-2 installation steps
Latch sub[27]
Mandrel[36]

## Slide 46: Tool maintenance process
3-2 installation steps
3-2-4 Connect the mandrel [36] to the collet sub [24]
Mandrel[36]
Collet sub [24]

## Slide 47: Tool maintenance process
3-2 installation steps
3-2-5 Connect the [27] to the collet sub [24]
Collet sub [24]
Latch sub[27]

## Slide 48: Tool maintenance process
Mandrel[36]
Poppet housing[40]
Poppet spring[31]
3-2 installation steps
3-2-6 Pass the spring [31] from the right end of the mandrel [36] and push it into the poppet housing [40]]

## Slide 49: Tool maintenance process
3-2 installation steps
3-2-7 Connect the delayed inflate ring [37] through the shear pin [16] and the spring housing [29]
Spring housing[29]
Delayed inflate ring[37]
Shear screw[16]

## Slide 50
3-2 installation steps
3-2-8 Connect the spring housing [29] and the poppet housing [40]
Spring housing[29]
Poppet housing[40]
Tool maintenance process

## Slide 51: Tool maintenance process
3-2 installation steps
3-2-9 The connection of the joint on the [29] and the expansion valve sleeve [40] is completed
Spring housing[29]
Poppet housing[40]

## Slide 52: Tool maintenance process
3-2 installation steps
3-2-10 Pass the element [32] from the right end of the mandrel [36] and connect it with the upper joint [29]. Pay attention to distinguish the upper and lower ends of the Element. method: At this time, when holding the buckle on the plastic bucket by hand, the opening direction of the steel strip is opposite to that of the hand, and the feeling is rough; when the shackle is buckled, the opening direction of the steel strip is the same as the direction of the hand movement, and the feeling is smooth.
Spring housing[29]
Element[32]

## Slide 53: Tool maintenance process
3-2 installation steps
3-2-11 Pass the bottom sub [33] through the right end of the mandrel [36] and connect it with the lower end of the element [32].
Element[32]
Bottom sub[33]
Mandrel[36]

## Slide 54: Tool maintenance process
3-2 installation steps
3-2-12 Install the bleeder plug [34]on the bottom sub [33].
Bleeder plug[34]

## Slide 55: Tool maintenance process
3-2 installation steps
3-2-13 Place the shear ring [58] inside the shear adapter[57] and secure with shear screw [56].
Shear adapter[57]
Shear screw[56]
Shear ring [58]

## Slide 56: Tool maintenance process
3-2 installation steps
3-2-14 Connect the shear connector [57] to the bottom sub [33]. Be careful not to tighten at this time to prevent damage to the shear screw.
Shear adapter[57]
Bottom sub[33]

## Slide 57: Tool maintenance process
3-2 installation steps
3-2-15 Connect the shear sub [42] and the ball seat [45]
Ball seat[45]
Shear sub[42]

## Slide 58: Tool maintenance process
3-2 installation steps
3-2-16 Connect the shear sub[42] to the ball seat catcher [44]
Shear sub[42]
Seat catcher[44]

## Slide 59: Tool maintenance process
Shear screw[18]
Seat catcher[44]
3-2-17 Attach the shear pin [18] to the seat catcher [44]
3-2 installation steps

## Slide 60: Tool maintenance process
3-2 installation steps
3-2-18 Connect the shear sub section [42] and the mandrel [36]
Shear sub[42]
Mandrel [36]

## Slide 61: Tool maintenance process
Pull release sleeve[23]
Latch sub[27]
Shear screw [38]
3-2-19 At the other end of the tool, the pull release sleeve [23] is secured to the latch sub [27] via a shear pin [38]. As shown below. The number of pins here determines the lifting force required when the packer is unsealed
3-2 installation steps

## Slide 62: Tool maintenance process
3-2 installation steps
3-2-20 Place the split ring [28] into the pull release sleeve [23] and secure it with oil. Pay attention to the direction of the snap ring, as shown below
Split Ring[28]
Pull release sleeve[23]

## Slide 63: Tool maintenance process
3-2 installation steps
3-2-21 Connect the upper mandrel connector[21] and pull release sleeve [23]. Shock-absorbing spindle surface is a sealing surface
upper mandrel connector[21]
pull release sleeve [23]

## Slide 64: Tool maintenance process
piston [22]
upper mandrel connector[21]
3-2 installation steps
3-2-22 Install the piston [22] to the upper mandrel connector[21]

## Slide 65: Tool maintenance process
3-2 installation steps
3-2-23 Insert Upper mandrel[30] to upper mandrel connector[21]
upper mandrel [30]
upper mandrel connector[21]

## Slide 66: Tool maintenance process
3-2 installation steps
Bumper Housing [20]
collet sub [24]
upper mandrel [30]
3-2-24 Slide Bumper Housing[20] to collet sub[24]

## Slide 67: Tool maintenance process
3-2 installation steps
3-2-25 Insert the end cap [19] to the Bumper Housing[20]
End Cap (19)
Bumper Housing (20)
upper mandrel [30]

## Slide 68: Tool maintenance process
Equalizing sub(64)
Equalizing sleeve(61)
3-1 Removal steps
3-2-26 the view of Equalizing sub [64] Equalizing sleeve[61], insert the equalizing sleeve into the equalizing sub.

## Slide 69: Tool maintenance process
Equalizing sub connector(65)
upper Mandrel
3-2 Installation steps
3-2-27 Tighten the Equalizing sub Connector [65] to the upper mandrel[30]

## Slide 70: Tool maintenance process
3-2 installation steps
3-2-28 Tighten the Equalizing sub[64] to the Equalizing sub connector[]
Equalizing sub connector(65)
Equalizing sub(64)

## Slide 71: Tool maintenance process
Equalizing sub(64)
shear screw (17)
3-2 installation steps
3-2-29 Tighten the shear screw [17] to the Equalizing sub[64]

## Slide 72: Tool maintenance process
3-2 installation steps
3-2-30 Tighten the fishing neck [60] to the Equalizing sub[64]
fishing neck (60)
Equalizing sub (64)

## Slide 73
End Of Maintenance
Maintenance completely

## Slide 74: End Of Maintenance
Apply a small amount of butter to all the exposed threads and holes in the tool. Wear wire on both ends of the tool; Move the test pressure qualified tool to the qualified equipment area. Remove the pressure record card and fill in the relevant information (country, region, field name, well name, tool name, date, time, etc.). Fill in the tool maintenance record form, and the coiled tubing engineer must sign and confirm it. Fill in the tool status label and attach it to the wire. Neatly tidy tools, remove safety signs and warning tapes, report forms and drawings, provide convenience for next operation, and clean wastes, such as old seals, on the spot according to waste disposal regulations.

## Slide 75: End Of Maintenance
For different sizes of set internal diameters, the packer is subject to different pressure values. It is necessary to select the appropriate number of shear pins according to the well conditions. Specific need to query the tool data sheet (Data sheet). The following table shows the working pressure values in the manual for each shear pin value.

## Slide 76: End Of Maintenance
Shear pin number selection

## Slide 77: Tool maintenance process
3.1 Inspect all O-rings on each component for damage.
3.2 After using diesel oil to remove oil from the components of the tool, clean it with clean water and blow it with compressed air, especially to ensure that the inner wall of the tool barrel is clean.
3.3 Check all parts for damage.
3.4 Replace the damaged part and record the part number of the newly replaced part on the maintenance log sheet.
3.5 Apply a little oil on the surface of each spring and O-ring

## Slide 78
4- End of maintenance
4-1 Tool disposal
4-1-1 Apply a small amount of butter to all the exposed threads and holes in the tool
4-1-2 Wear wire on both ends of the tool
4-1-3 pressure test the tools
4-2 fill in the document
4-2-1 remove the pressure record card and fill in relevant information (country area, oilfield name, well name, tool name, date, time, etc.)
4-2-2 Fill in the tool maintenance record form, CTU engineers must sign and confirm
4-2-3 Fill in the tool status label and attach it to the wire

## Slide 79: End Of Maintenance
Apply a small amount of butter to all the exposed threads and holes in the tool. Wear wire on both ends of the tool; Move the test pressure qualified tool to the qualified equipment area. Remove the pressure record card and fill in the relevant information (country, region, field name, well name, tool name, date, time, etc.). Fill in the tool maintenance record form, and the coiled tubing engineer must sign and confirm it. Fill in the tool status label and attach it to the wire. Neatly tidy tools, remove safety signs and warning tapes, report forms and drawings, provide convenience for next operation, and clean wastes, such as old seals, on the spot according to waste disposal regulations.

## Slide 80: End Of Maintenance
Note: The tool status label is divided into 3 colors
The green card indicates that the maintenance of the tool, pressure test, and function test are completed. The status is good and can be used.

## Slide 81: End Of Maintenance
The yellow card indicates that there are some minor problems in the process of tool maintenance, pressure test, and debugging. However, after the repair or re-maintenance, the function can be restored and reused.

## Slide 82: End Of Maintenance
Red card indicates that the tool has been irreparably damaged and can no longer be used

## Slide 83
5- Finishing work
Neatly tidy up the tools, remove safety signs and warning tapes, and archive reports and drawings to facilitate the next operation. Clean wastes and other waste seals in accordance with waste disposal regulations.

## Slide 84
Thanks for your attention