## Slide 1
2017.02
Baker Hydraulic Release Overshot
Document No:00
Editor: Jalal Alali

## Slide 3
CONTENT
Introduction of Baker Hydraulic Release Overshot
Disassembly
Assembly
Baker Hydraulic Release Overshot معرفی
نحوی جدا سازی قطعات
نحوی سر هم کردن قطعات

## Slide 6
Introduction:
معرفی:
The Hydraulic Relese Overshot Hs Been Designed To Allow Engagement With A Fish Having A Standard External Type Wireline Fishing Neck Looking Up. The Hydraulic Release Overshot Was Designed With Pump Through Capabilities Specifically For Coiled Tubing Applications. The Overshot Is Latched Up To The Fishing Neck By Applying Alight Set Down Weight At The Tool. If The Fish Can Not Be Freed, the Overshot May Be Released From The Fishing Neck By Flowing Through The Workstring. This Feature Prevents Having To Leave Any Part Of The Fishing Tool String If The Fish Is Left In The Hole. Leaving Any Part Of The Fishing String In The Hole Will Hamper Subsequent Fishing Operations.
The Hydraulic Release Overshot Has Been Designed To Be Used With Jaring Systems And Is Able To Handle Haigh Impact Loads Imparted By The Jar. The Design Uses A Collet Grapple To Latch Up To The Fishing Neck, However The Collet Fingers are Not Subjected To Tensile Loading.

## Slide 7
Required hand tools
ابزار مورد نیاز
Pipe Wrench
Allen Key
Rubber Hammer
Bowl
Flat Bar

## Slide 8
Disassembly
Place Top Sub In Vice

## Slide 9
A
B
Unscrew Body From Top Sub

## Slide 10
A
B
Remove The Body From The Assembly

## Slide 11
A
B
Reach Inside The Grapple With A HEX Socket (Allen) And Engage The HEX In The End Of The Mandrel

## Slide 12
A
B
Break Out The Thread Between The Top Sub And The Mandrel

## Slide 13
A
B
Remove The Spring From The Top Sub , Then Remove The Grapple From The Mandrel

## Slide 14
A
B
Unsrew The Orifice Retainer From The Mandrel And Unload The Orifive From The Mandrel

## Slide 15
A
B

## Slide 16
Assembly
Install the Orifice Inside The End Of The Mandrel And Secure It In Place With The Orifice Retainer

## Slide 17
A
B
Slide Grapple Over End Of The Mandrel Untill The Grapple Bottoms Out
* Note: During Doing This It Will Be Necessary To Deflect The Grapple’s Fingers Outward To Pass Over Large OD Section Of The Mandrel (It Will Prevent Damage To O-ring).

## Slide 18
A
B
Place Top Sub In Vice, Then Slide Spring Over Recessed End Of Top Sub

## Slide 19
A
B
Place Pin End Of Mandrel Through Spring And Make Up To Top Sub
* Note: Tighten This joint By Using A HEX Socket With An Extension

## Slide 20
A
B
Once This Joint Is Tightened, Check To Make Sure The Grapple Is Free To Move Against Yhe Spring By Stroking It By Hand

## Slide 21
A
B
Make Up Body To Top Sub

## Slide 22
A
B